## Slide 1: FTM + GPS Anchor Based AP Localization
Multilateration and Joint Optimization for Wi‑Fi AP Localization
IEEE 802.11mc Fine Timing Measurement
wenhan zhang

## Slide 2: Motivation
- Accurate AP localization for network optimization
- Required for MAB-based Wi‑Fi control
- RSSI-only methods insufficient

## Slide 3: IEEE 802.11 FTM Overview
- Introduced in IEEE 802.11mc
- Measures RTT between nodes
- Provides range-only information

## Slide 4: Multilateration Equations
FTM distance:
dᵢ = (c × RTTᵢ) / 2
Range constraint:
||p − aᵢ||² = dᵢ²
Solve via Least Squares / WLS

## Slide 5: Multilateration Geometry (2D Example)
A
A
A
AP

## Slide 6: Localization Algorithm (Pseudo-Code)
Collect FTM RTTs from anchors
Convert RTT → distance
Form A, b matrices
Solve A x = b using SVD
Return estimated AP position

## Slide 7: ns-3 Implementation Details
- MobilityModel provides ground truth
- Custom FTM RTT generator
- Inject Gaussian + NLOS bias
- Eigen-based solver module
- RMSE evaluation

## Slide 8: Multi-AP Joint Localization
- Nodes: anchors + unknown APs
- Edges: FTM ranges
- Graph-based optimization
- Solved via iterative least squares

## Slide 9: FTM vs RSSI vs AoA
FTM:
- Meter-level accuracy
- RTT-based
RSSI:
- Low cost
- Highly unstable
AoA:
- High accuracy
- Requires antenna arrays

## Slide 10: Results (Template)
Metrics:
- Localization RMSE
- CDF of error
Parameters:
- Number of anchors
- NLOS probability
- Noise variance

## Slide 11: Conclusion and Future Work
- FTM + GPS enables accurate AP localization
- Joint localization improves robustness
- ns-3 supports reproducible evaluation
- Future: EKF, factor graphs, real testbeds